## Slide 1: 104年度第二次 台北區網(臺大)網管會議
臺灣大學計資中心
游子興
davisyou@ntu.edu.tw
3366-5008

## Slide 2: 區網連外架構圖

## Slide 10: IPS 誤擋
國防大學網頁被中央區網 IPS 誤擋

## Slide 11: IPS 誤擋
執行網頁查詢後
執行網頁查詢後

## Slide 12: IPS 誤擋
3分鐘後恢復連線

## Slide 13: 中央區網 IPS 訊息
Palo Alto 5060
  HTTP SQL Injection Attempt
  ID
  30514
  Description
  SQL injection is a technique that exploits a security vulnerability occurring in the database layer of an application. The vulnerability is present when user input is either incorrectly filtered for string literal escape characters embedded in SQL statements or user input is not strongly typed and thereby unexpectedly executed. It is in fact an instance of a more general class of vulnerabilities that can occur whenever one programming or scripting language is embedded inside another.

## Slide 14: Unicast Flooding
  網路設備為 Switch 非 Hub 之情況下，執行 Wireshark 抓取封包
  電腦 IP位址: 140.112.3.82
  卻出現非自己 IP 之 Unicast 封包

## Slide 15: Unicast Flooding
發生原因
Case1. 綁定 ip & mac, 但此 mac address 目前不存在 mac address table
  (config)# arp 140.112.3.114 14da.e997.1356 ARPA
  # sh ip arp 140.112.3.114
  Protocol Address Age (min) Hardware Addr Type Interface
  Internet 140.112.3.114 - 14da.e997.1356 ARPA
  # sh mac address-table address 14da.e997.1356
  vlan mac address type learn age ports
  ------+----------------+--------+-----+----------+--------------------------
  No entries present.

## Slide 16: Unicast Flooding
Case2. arp table 尚未 Timeout, 但 mac address table 已經 timeout
  # sh ip arp 140.112.3.77
  Protocol Address Age (min) Hardware Addr Type Interface
  Internet 140.112.3.77 213 e0cb.4e7a.fb99 ARPA Vlan304
  # sh mac address-table address e0cb.4e7a.fb99
  vlan mac address type learn age ports
  ------+----------------+--------+-----+----------+--------------------------
  No entries present.
The default ARP table aging time is 4 hours while the Content Addressable Memory (CAM) holds the entries for only 5 minutes

## Slide 17: Unicast Flooding
測試從 Hinet IP: 114.34.121.216
  ICMP: ping 140.112.3.77
  TCP: telnet 140.112.3.77 80

## Slide 18: Unicast Flooding 解決方法
方法一:
  You need a CAM aging timer greater or equal to the ARP timeout in order to prevent unicast flooding.
  (config)# mac-address-table aging-time xxxx
方法二:
  Enables unknown unicast or multicast flood blocking on the port.
  (config)#int g8/26
  (config-if)#switchport block unicast
  若一個 Vlan 包含許多 Interface, 則每個 Interface 皆須下此指令

## Slide 19: 一個 Vlan 中含太多網段
多個網段同屬相同 Broadcast Domain
  Broadcast 所佔頻寬大
  容易因 arp flooding 攻擊造成網路癱瘓
Vlan 切割前
  interface Vlan1
    ip address 140.112.16.254 255.255.255.0 secondary
    ip address 140.112.32.254 255.255.255.0 secondary
    ip address 140.112.37.254 255.255.255.0 secondary
    ip address 140.112.40.254 255.255.255.0 secondary
    ip address 140.112.43.254 255.255.255.0 secondary
    ip address 140.112.46.254 255.255.255.0 secondary
    ip address 140.112.15.62 255.255.255.192 secondary
    ip address 140.112.44.62 255.255.255.192 secondary
    ip address 140.112.14.254 255.255.255.0
Vlan 切割後
  interface Vlan37
    ip address 140.112.37.254 255.255.255.0

## Slide 20: 一個 Vlan 中含太多網段
切割 Vlan 前後之網路流量
切割前
切割後

## Slide 21: IP 結尾 .0 .255 是否合法
遠傳 ADSL 使用者反應使用 IP: 110.28.31.0 無法連上台大網站
Traceroute 測試
  110.28.31.0 vs.110.28.31.1
教育部對外 ISP Router

## Slide 22: IP 結尾 .0 .255 是否合法
www.amazon.co.jp 網站結尾也是 .0
阻擋之 ACL:
  deny ip any 0.0.0.0 255.255.255.0
    阻擋目的 IP: X.X.X.0 (0 結尾 ip)
  deny ip any 0.0.0.255 255.255.255.0
    阻擋目的 IP: X.X.X.255 (255 結尾 ip)

## Slide 23: IP 結尾 .0 .255 是否合法
將台大IP: 140.112.0.0/255.255.0.0 直接當成一個 Class B 使用
  網路位址: 140.112.0.0
  廣播位址: 140.112.255.255
  合法主機位址: 140.112.0.1~140.112.255.254
    因此下列位址可以被分配給主機
    140.112.1.0、140.112.2.0 …
    140.112.1.255、140.112.2.255 …
為何 ISP 要使用大於 Class C 之網段?

## Slide 24: Traceroute in Window/Linux
關於 Traceroute 在 Window 與 Linux 結果不同的原因在於兩個作業系統之 Traceroute 使用之偵測封包不同.
Window 預設使用 ICMP 而 Linux 預設使用 UDP, 而 UDP 偵測可能被 Router 阻擋而不回應.
Linux 可加 -I 參數 強制使用 ICMP 封包, Traceroute 路徑即可順利走完.

## Slide 25: Traceroute in Window/Linux

## Slide 26: Akamai 下載測試 (Hinet)
Notes: a23-53-65-123.deploy.static.akamaitechnologies.com

## Slide 27: Akamai 下載測試 (教育部)
Notes: a23-77-20-199.deploy.static.akamaitechnologies.com