## Slide 1: Cache Server 國際頻寬 POC
報告人：游子興
Email：davisyou@ntu.edu.tw
電話：02-33665008
日期：2016/11/2

## Slide 2: 台大CF5000 測試架構
 | Net1 IP Addr | Net2 IP Addr | Net3 IP Addr
N7K WAN2 Eth1/23 | 172.16.1.1/30 | No | No
N7K WAN1 Eth1/23 | No | 172.16.1.5/30 | No
A10 | 172.16.1.2/30 | 172.16.1.6/30 | 140.112.149.33/30
CF5000 MGT | No | No | 140.112.149.34/30
internet
國際頻寬
1G * 2
WAN 1 Router
WAN 2 Router
ASCC
TANet
Net1
Net2
GE UTP * 4
CF5000
N7K WAN1
N7K WAN2
Vlan 981
Vlan 982
Eth1/15
Eth1/15
N7K LAN1
N7K LAN2
Eth1/23
Eth1/23
CF5000
GE UTP * 4

## Slide 3: Police Based Routing(PBR)
interface vlan 981
  ip policy route-map CF5K1
route-map CF5K1 permit
  match ip address CF5K-ACL1
  set ip next-hop 172.16.1.6
ip access-list extended CF5K-ACL1
  10 permit tcp any eq www 140.112.3.82/32
  20 permit tcp any eq www 140.112.4.0/24
Vlan 981
Eth1/15
WAN1
N7K WAN1
Blue Coat
Cache Server
172.16.1.6
N7K LAN1

## Slide 4: Police Based Routing(PBR)
interface Eth 1/15
  ip policy route-map CF5K2
route-map CF5K2 permit
  match ip address CF5K-ACL2
  set ip next-hop 172.16.1.6
ip access-list extended CF5K-ACL2
  10 permit tcp 140.112.3.82/32 any eq www
  20 permit tcp 140.112.4.0/24 any eq www
Vlan 981
Eth1/15
WAN1
140.112.0.206
N7K WAN1
140.112.0.190
Blue Coat
Cache Server
172.16.1.6
N7K LAN1
140.112.0.170

## Slide 5: Trace Route – ICMP
傳統 tracert 使用 ICMP
非 TCP 80 port，不受PBR影響

## Slide 6: Trace Route – TCP port 80
使用 tracetcp.exe TCP 80 port，受PBR影響
封包導入A10 + Blue Coat

## Slide 7: Trace Route – TCP port 443
使用 tracetcp.exe TCP 443 port，不受PBR影響

## Slide 8: 國際頻寬下載 Source Port 分析
2016/11/4 08:00~16:00
69%
22%

## Slide 9: Cache Server 上線時間
暑假期間
  2016/7/19(一) 09:00 ~ 2016/7/21(三) 12:00
開學前後
  2016/9/7 (三) 09:00~ 2016/9/26(一)09:00

## Slide 10: 國際頻寬用量比較 - By Day 7/19~7/21 CacheServer 上線
國際頻寬
明顯減少
Cache Server 上線
2016/7/19

## Slide 11: MRTG Log 前後兩週比較 7/19~7/21 CacheServer 上線
前後兩週: 週二 ~ 週四 國際頻寬 用量比較
紅色: 7/12 00:00 ~ 7/14 12:00
藍色: 7/19 00:00 ~ 7/21 12:00
Cache Server 上線頻寬為前一週 77.9%, 節省 22.1%

## Slide 12: 國際頻寬用量比較- By Week 9/7~9/26 CacheServer 上線
Cache Server 上線
國際頻寬
明顯增加
2016/9/7
2016/9/26
2016/9/12 開學

## Slide 13: 國際頻寬用量比較- By Day 9/7~9/26 CacheServer 上線
Cache Server 停止
國際頻寬
明顯增加
2016/9/26

## Slide 14: 國際頻寬用量比較 上學期 vs 本學期
上學期與本學期: 週一 ~ 週日 國際頻寬 用量比較
紅色(上學期): 2016/5/16 ~ 2016/5/22
綠色(本學期): 2016/9/19 ~ 2016/9/26
Cache Server 上線頻寬為上學期 67%, 節省 33.3%

## Slide 15: Access Log分析
2016/9/14 9:00~17:00
筆數: 82,537,267
原始 log: 35.7 GB
Elasticseach空間: 278.6 GB

## Slide 16: Access Log example
140.112.22.222 連線 http://www.chinatimes.com/images/ct-logo-8585.jpg
140.112.27.247 連線 http://www.chinatimes.com/scripts/hometopnews12.js?sdate=201609141157

## Slide 17: Access Log 欄位說明
c-ip: client's IP
sc-status: Protocol status code from appliance to client
sc-bytes: bytes from server to client
cs-bytes: bytes from client to server
rs-bytes: bytes from web to server
sr-bytes: bytes from server to web
s-action: What type of action did the Appliance take to process this request
  TCP_HIT
  TCP_NC_MISS
  TCP_CLIENT_REFRESH
  TCP_MISS

## Slide 18: Access Log 欄位說明
cs-method: Request method
  GET
  POST
  HEAD
cs-uri-path: URL Hostname 之後不包含 GET 串
cs-uri-query: URL Hostname 之後 GET 字串
cs-uri-extension: 附檔名
cs(User-Agent): Client browser
cs-ip: web site ip

## Slide 19: 2016/9/14
Cache to Client (Client download) | Web to Cache (Server download) | Cache rate %
10,593,456,752,577 | 4,984,419,542,731 | 52.95

## Slide 20: 2016/9/14

## Slide 21: 每30 分鐘 Cache rate %分析
timestamp | Cache to Client | Web to Cache | Cache rate %
08:50:00.000 | 12,509,907,809 | 2,315,340,869 | 81.49
09:00:00.000 | 157,515,218,856 | 46,597,735,874 | 70.42
09:10:00.000 | 169,501,163,741 | 49,810,032,475 | 70.61
09:20:00.000 | 151,211,348,234 | 53,269,467,694 | 64.77
09:30:00.000 | 166,379,508,053 | 55,519,411,121 | 66.63
09:40:00.000 | 155,883,972,814 | 45,816,603,551 | 70.61
09:50:00.000 | 166,376,359,852 | 55,252,708,496 | 66.79
10:00:00.000 | 238,982,097,868 | 108,061,871,145 | 54.78
10:10:00.000 | 238,048,729,085 | 111,323,902,056 | 53.23
10:20:00.000 | 238,964,746,065 | 98,637,605,641 | 58.72
10:30:00.000 | 247,227,493,509 | 119,212,703,267 | 51.78
10:40:00.000 | 234,999,023,462 | 107,630,703,233 | 54.2
timestamp | Cache to Client | Web to Cache | Cache rate %
10:50:00.000 | 236,258,330,436 | 111,195,773,686 | 52.93
11:00:00.000 | 251,732,664,167 | 121,478,383,051 | 51.74
11:10:00.000 | 249,920,937,713 | 111,298,493,282 | 55.47
11:20:00.000 | 251,193,904,444 | 104,094,785,198 | 58.56
11:30:00.000 | 271,766,411,815 | 126,327,296,115 | 53.52
11:40:00.000 | 233,039,482,853 | 105,603,300,792 | 54.68
11:50:00.000 | 230,838,311,892 | 103,185,625,480 | 55.3
12:00:00.000 | 222,265,770,752 | 103,592,226,128 | 53.39
12:10:00.000 | 221,214,224,203 | 99,622,454,836 | 54.97
12:20:00.000 | 192,041,311,691 | 90,014,515,930 | 53.13
12:30:00.000 | 212,385,061,101 | 103,905,963,831 | 51.08
12:40:00.000 | 214,600,531,686 | 108,655,646,736 | 49.37

## Slide 22: 每30 分鐘 Cache rate %分析
timestamp | Cache to Client | Web to Cache | Cache rate %
12:50:00.000 | 200,541,781,394 | 101,075,206,012 | 49.6
13:00:00.000 | 218,456,187,067 | 106,703,041,275 | 51.16
13:10:00.000 | 217,614,854,792 | 111,993,277,521 | 48.54
13:20:00.000 | 230,469,375,863 | 110,636,617,139 | 52
13:30:00.000 | 246,147,323,362 | 123,122,762,449 | 49.98
13:40:00.000 | 239,587,903,084 | 121,132,281,936 | 49.44
13:50:00.000 | 230,425,462,865 | 113,389,160,925 | 50.79
14:00:00.000 | 315,748,831,238 | 181,196,123,149 | 42.61
14:10:00.000 | 178,548,544,404 | 88,928,071,046 | 50.19
14:20:00.000 | 200,588,071,585 | 99,399,586,194 | 50.45
14:30:00.000 | 224,417,793,992 | 116,136,714,353 | 48.25
14:40:00.000 | 200,241,004,890 | 102,223,587,556 | 48.95
timestamp | Cache to Client | Web to Cache | Cache rate %
14:50:00.000 | 202,233,677,577 | 109,891,197,817 | 45.66
15:00:00.000 | 214,840,773,098 | 107,294,115,385 | 50.06
15:10:00.000 | 213,675,629,736 | 98,830,366,947 | 53.75
15:20:00.000 | 204,443,105,943 | 91,016,112,659 | 55.48
15:30:00.000 | 242,765,897,661 | 126,429,196,510 | 47.92
15:40:00.000 | 224,509,046,149 | 108,082,409,247 | 51.86
15:50:00.000 | 224,273,220,168 | 117,958,664,251 | 47.4
16:00:00.000 | 226,201,890,935 | 113,608,726,770 | 49.78
16:10:00.000 | 230,497,856,972 | 115,090,159,993 | 50.07
16:20:00.000 | 240,088,935,238 | 119,446,769,975 | 50.25
16:30:00.000 | 238,565,203,621 | 125,615,337,756 | 47.35
16:40:00.000 | 239,932,736,851 | 125,381,275,815 | 47.74

## Slide 23: Top 20 Hosts

## Slide 24: Top 20 Hosts 佔所有頻寬 %
*.apple.com=23%
*.windowsupdate.com=22%
hichannel
廣播

## Slide 25: Address Dynamic Web 2.0 Content
Identify same content, independent of file name or URL
  Object metadata support
  Site-specific rules & instructions
Cloud-based updates via CachePulse™
  Address new & emerging popular sites
  Respond to changes in content delivery on existing sites
  Updates available on 20-minute basis
  Customer feedback loop via heartbeats

## Slide 26: Cache Media & Video
Supports any audio/video file served over HTTP
  Progressive download/play
  Flash, HTML5

## Slide 27: Twitch.tv - Live streaming video Online Game

## Slide 28: Twitch.tv
原廠文件提供測試文件

## Slide 29: Twitch.tv 實際測試 Cache Rate%
Top | URL Host | Cache to Client (Client) | Web to Cache (Server) | Cache rate %
1 | player.twitch.tv | 29,304,731 | 29,492,779 | -0.64
2 | minixperiment.twitch.tv | 3,944,493 | 270,707 | 93.14
3 | usher.twitch.tv | 2,156,367 | 2,156,382 | 0
4 | spade.twitch.tv | 1,390,526 | 1,390,852 | -0.02
5 | api.twitch.tv | 765,352 | 659,111 | 13.88
6 | www.twitch.tv | 340,208 | 340,208 | 0
7 | status.twitch.tv | 134,513 | 79,883 | 40.61
8 | spectre.twitch.tv | 77,372 | 63,363 | 18.11

## Slide 30: Twitch.tv 實際測試 Cache Rate %
Top | URL Host | Cache to Client (Client) | Web to Cache (Server) | Cache rate %
9 | irc-ws.chat.twitch.tv | 60,424 | 46,956 | 22.29
10 | twitch.tv | 54,614 | 40,773 | 25.34
11 | countess.twitch.tv | 12,950 | 12,390 | 4.32
12 | zh-tw.twitch.tv | 9,149 | 9,149 | 0
13 | help.twitch.tv | 456 | 456 | 0
14 | fan.twitch.tv | 408 | 0 | 100
15 | link.twitch.tv | 319 | 295 | 7.52
 | 加總 | 38,317,596 | 34,627,242 | 9.63

## Slide 31: 簡報完畢 謝謝