## Slide 1: pfSense Case Study
游子興
台大計中網路組
davisyou@ntu.edu.tw
02-33665008

## Slide 2: pfSense
http://pfsense.org/

## Slide 3: 測試架構
Vmware ESXi

## Slide 4: Topic
NAT Mode
NAT Mode with Many Public IPs
Route Mode
  Router
  Firewall
NAT Mode with Multi-WAN
  Load Balance
  Policy Base Routing
Route/NAT Mode with Multi-WAN
Overall
  LAN -> DMZ
  使用 Static Route 簡化設定
Site to Site VPN
  OpenVPN
  IPsec

## Slide 5: NAT Mode

## Slide 6: NAT Mode
TANet
pfsense
WANTANET
192.192.7.122/30
192.192.7.121/30
LAN
192.168.200.1/24
PC1
IP:192.168.200.2/24
GW:192.168.200.1
PC2
IP:192.168.200.3/24
GW:192.168.200.1
PC3
IP:192.168.200.4/24
GW:192.168.200.1
Public IP
Private IP

## Slide 7: Interface: WANTANET

## Slide 8: Interface: LAN

## Slide 9: Firewall > Rules > WAN
外對內預設全部拒絕，不需設定

## Slide 10: Firewall > Rules > LAN
LAN to any 預設全部允許，不需設定

## Slide 11: Firewall > NAT > Outbound
使用預設值
  Automatic outbound NAT rule generation.

## Slide 12: Services > DHCP Server > LAN
開啟 DHCP 服務 on LAN Interface

## Slide 13: 測試結果

## Slide 14: NAT Mode Many Public IP (Virtual IP)

## Slide 15: NAT Mode Many Public IPs
TANet
pfsense
WANTANET
192.192.7.122/30
192.192.7.121/30
LAN
192.168.200.1/24
PC1
IP:192.168.200.2/24
GW:192.168.200.1
PC2
IP:192.168.200.3/24
GW:192.168.200.1
PC3
IP:192.168.200.4/24
GW:192.168.200.1
Virtual IPs for NAT
140.131.0.128/25
Public IP
Private IP
Public IP

## Slide 16: Firewall > Virtual IPs

## Slide 17: Firewall > NAT > Outbound
改成 Manual Outbound NAT rule generation

## Slide 18: Firewall > NAT > Outbound

## Slide 19: 測試結果

## Slide 20: Route Mode

## Slide 21: Route Mode
TANet
pfsense
WANTANET
192.192.7.122/30
192.192.7.121/30
DMZ
140.131.0.1/25
PC1
IP:140.131.0.2/25
GW:140.131.0.1
PC2
IP:140.131.0.3/25
GW:140.131.0.1
PC3
IP:140.131.0.4/25
GW:140.131.0.1
Route Mode
Public IP
Public IP

## Slide 22: Interface: DMZ

## Slide 23: 方法一 Router

## Slide 24: System -> Advanced -> Firewall & NAT
converts pfSense into a router
turn off Firewall & NAT

## Slide 25: 測試結果

## Slide 26: 測試結果
From Hinet to 140.131.0.2

## Slide 27: 方法二 FirewalL

## Slide 28: Firewall > Rules > WANTANET
Internet to DMZ IP(140.131.0.0/24) 全部開放
  any to DMZ全部開放
1

## Slide 29: Firewall > Rules > WANTANET

## Slide 30: Firewall > Rules > DMZ
DMZ to any 全部開放

## Slide 31: Firewall > Rules > DMZ

## Slide 32: Firewall > NAT > Outbound
Disable Outbound NAT rule

## Slide 33: 測試結果

## Slide 34: pfsense 管理 IP 問題
使用 Public IP: 140.131.0.1 可直接連到 pfsense 管理介面
解決方法:
  Firewall > Rules > WANTANET
  拒絕: Any to DMZ address

## Slide 35: Firewall > Rules > WANTANET
Block: the packet is dropped silently.
Reject: a TCP RST or ICMP port unreachable for UDP is returned to the sender.

## Slide 36: NAT Mode Multi-WAN

## Slide 37: NAT & Multi-WAN
TANet
pfsense
WANTANET
192.192.7.122/30
192.192.7.121/30
LAN
192.168.200.1/24
PC1
IP:192.168.200.2/24
GW:192.168.200.1
NTU
WANNTU
140.112.3.105/25
140.112.3.126/25
PC2
IP:192.168.200.3/24
GW:192.168.200.1
PC3
IP:192.168.200.4/24
GW:192.168.200.1
Public IP
Public IP
Private IP

## Slide 38
Case1: Load Balance
  內對外輪流由兩個 WAN 出去
Case2: Policy Base Routing
  內對外依據 Destination IP 決定由哪個 WAN 出去
Destination IP | WAN IP
140.112.0.0/16 | 140.112.3.105
其他 | 192.192.7.122

## Slide 39: Interface: WANNTU

## Slide 40: Firewall > Rules > WANNTU
外對內預設全部拒絕，不需設定

## Slide 41: System > Routing > Gateways
列出 “Interfaces: IPv4 Upstream gateway” 有設定之 Gateways
Default Gateway
  僅能有一筆 Check
  影響 Diagnostics -> Routes 之 Default Route

## Slide 42: Weight (用於 Gateway Group)
If 2 gateway one is a 500Mbps and another is a 100Mbps, a 5:1 ratio of usage to prefer the faster WAN on the same tier.
  500Mbps: Weight=5
  100Mbps: Weight=1

## Slide 43: Diagnostics -> Routes

## Slide 44: Case1 Load Balance

## Slide 45: Gateway Group

## Slide 46: Link Priority/Tier
The lower tier numbers are preferred.
If two gateways are on the same tier, they will load balance.
In different tiers, they will do failover preferring the lower tier.

## Slide 47: Firewall > Rules > LAN
將 Gateway 設定為 Gateway Group

## Slide 48: 測試結果

## Slide 49: 測試結果
第一跳皆少了 192.168.200.1

## Slide 50: Case2 Policy Base Routing

## Slide 51: Firewall > Rules > LAN
Policy Base Routing
  by Destination IP

## Slide 52: Destination = 140.112.0.0/16

## Slide 53: Destination = any

## Slide 54: 測試結果

## Slide 55: 測試結果
第一跳沒有 192.168.200.1，表示由 Firewall > Rules > LAN 已經決定 Next Hop，沒有查詢 Routing Table(Diagnostics -> Routes)

## Slide 56: RoutE/NAT Mode Multi-WAN Policy Base Routing

## Slide 57: Rout/NAT Mode Multi-WAN
TANet
pfSense
WANTANET
192.192.7.122/30
192.192.7.121/30
DMZ
140.131.0.1/25
PC1
IP:140.131.0.2/25
GW:140.131.0.1
PC2
IP:140.131.0.3/25
GW:140.131.0.1
PC3
IP:140.131.0.4/25
GW:140.131.0.1
NTU
WANNTU
140.112.3.105/25
140.112.3.126/25
Route Mode
Destination = others
NAT Mode
Destination = 140.112.0.0
TANet
Public IP
TANet
Public IP
NTU
Public IP

## Slide 58: Firewall > Rules > DMZ
Policy Base Routing
  by Destination IP

## Slide 59: Destination = 140.112.0.0/16

## Slide 60: Destination = any

## Slide 61: Firewall > NAT > Outbound
改成 Manual Outbound NAT rule generation

## Slide 62: Firewall > NAT > Outbound
Disable or Delete
  Interface:WANTANET & Source: 140.131.0.0/25

## Slide 63: 測試結果

## Slide 64: 測試結果
To NTU
To whatismyip.org

## Slide 65: Overall

## Slide 66: Overall
66
TANet
pfsense
WANTANET
192.192.7.122/30
192.192.7.121/30
DMZ
140.131.0.1/25
PCx
IP:140.131.0.x/25
GW:140.131.0.1
NTU
WANNTU
140.112.3.105/25
140.112.3.126/25
1.Destination = 140.112.0.0/16
to NTU, NAT Mode
2. Destination = any
to TANet , Route Mode
LAN
192.168.200.1/24
PCx
IP:192.168.200.x/24
GW:192.168.200.1
1.Destination = 140.112.0.0/16
to NTU, NAT Mode
2.Destination = any
to TANet, NAT Mode
Virtual IPs= 140.131.0.128/25
PCx
IP:140.131.0.x/25
GW:140.131.0.1
PCx
IP:140.131.0.x/25
GW:140.131.0.1
PCx
IP:192.168.200.x/24
GW:192.168.200.1
PCx
IP:192.168.200.x/24
GW:192.168.200.1
TANet
Public IP
Private IP

## Slide 67: LAN -> DMZ

## Slide 68: Firewall > Rules > LAN
Allow LAN -> DMZ

## Slide 69: Firewall > Rules > LAN

## Slide 70: Firewall > Rules > DMZ
DMZ -> LAN 沒有開放

## Slide 71: 測試結果
LAN -> DMZ
DMZ -> LAN

## Slide 72: 測試結果
LAN -> DMZ
DMZ -> LAN
  Match “Firewall > Rules > DMZ” 第二條 Gateway= TANETGW

## Slide 73: Ping Issue in Firewall Rule
如上結果從 DMZ 無法連線 LAN
但若先執行 ping LAN -> DMZ 有回應後，再 ping DMZ -> LAN，則也會有回應。
原因: 因為 ICMP 非 TCP 有 3 way handshake，pfSense 誤將 DMZ -> LAN 當成 LAN -> DMZ 之回應封包，因此通過 Rule.
建議用 TCP 連線測試較準確
  telnet IP:port
  遠端桌面

## Slide 74: 使用 Static Route 簡化設定

## Slide 75: 內對外連線
1. 決定 Next Hop/Gateway
  Firewall -> Rules -> Interface
  條件: Protocol、Source IP、Destination IP
  Gateway 值
    Default(無指定) --依據 Routing Table "Diagnostics -> Routes"
    指定gateway
2. 該 Gateway是否做 NAT 轉換
  Firewall -> NAT -> Outbound
  條件: Protocol、Source IP、Destination IP

## Slide 76: 使用 Static Route
若決定 Next Hop/Gateway
  Firewall -> Rules -> Interface 條件僅有 Destination IP
  則可用 Static Route 達成

## Slide 77: Firewall > Rules > LAN
原始預設值：LAN to any 全部允許
Gateway= default

## Slide 78: Firewall > Rules > DMZ
DMZ to any 全部允許
Gateway= default

## Slide 79: System > Routing > Static Routes
140.112.0.0/16 next hop to NTUGW

## Slide 80: System > Routing > Gateways
確認 Default Gateway= TANETGW

## Slide 81: Diagnostics -> Routes

## Slide 82: 測試結果
LAN/DMZ <-> Internet: OK
LAN -> DMZ: OK
DMZ -> LAN: OK

## Slide 83: From 192.168.200.2
第一跳有 192.168.200.1， 因為 Firewall > Rules > LAN: Gateway= default，需查詢 Routing Table(Diagnostics -> Routes)

## Slide 84: From 140.131.0.2
第一跳有 140.131.0.1，原因同上

## Slide 85: 台灣地區 IP位址核發列表
http://www.twnic.net.tw/
IP/ASN申請 > IPv4 位址查詢/統計 > IP位址核發列表
  http://rms.twnic.net.tw/twnic/User/Member/Search/main7.jsp?Order=ORG.ID

## Slide 86: www.twnic.net.tw

## Slide 87: Site to Site VPN
87
pfSense
TANet
163.28.16.45/24
PCx
IP:192.168.101.x/24
GW:192.168.101.1
pfSense
NTU
140.112.3.105/25
PCx
IP:192.168.200.x/24
GW:192.168.200.1

## Slide 88: OpenVPN Server(NTU) 端設定

## Slide 89: VPN > OpenVPN > Servers

## Slide 90: VPN > OpenVPN > Servers
設定一個未使用之 /30 網段
TANet 端使用之虛擬網段

## Slide 91: Firewall > Rules > WAN
允許來自 TANet IP 之連線

## Slide 92: Firewall > Rules > OpenVPN
OpenVPN to any 全部允許

## Slide 93: OpenVPN Client(TANet) 端設定

## Slide 94: VPN > OpenVPN > Clients
NTU 端 IP

## Slide 95: VPN > OpenVPN > Clients
Copy from Server 端之 Shared Key
設定一個未使用之 /30 網段
NTU 端使用之虛擬網段

## Slide 96: Firewall > Rules > OpenVPN
OpenVPN to any 全部允許

## Slide 97: Status > OpenVPN
觀察連線情況

## Slide 98: OpenVPN Client 端(TANet) redirect Gateway to 140.112.3.105

## Slide 99: Server Firewall > NAT > Outbound

## Slide 100: Client VPN > OpenVPN > Clients
Custom options:
  redirect-gateway def1;

## Slide 101: IPSEC TANet 端設定

## Slide 102: VPN > IPsec > Tunnels 192.168.101.1

## Slide 103: VPN > IPsec > Tunnels

## Slide 104: VPN > IPsec > Tunnels

## Slide 105: VPN > IPsec > Tunnels
NTU 端使用之虛擬網段

## Slide 106: Firewall > Rules > IPsec
IPsec to any 全部允許

## Slide 107: IPSEC NTU 端設定

## Slide 108: VPN > IPsec > Tunnels 192.168.200.1

## Slide 109: VPN > IPsec > Tunnels

## Slide 110: VPN > IPsec > Tunnels

## Slide 111: VPN > IPsec > Tunnels
TANet 端使用之虛擬網段

## Slide 112: Firewall > Rules > IPsec
IPsec to any 全部允許

## Slide 113: Status > IPsec > Overview

## Slide 114: IPsec TANet 端 redirect Gateway to 140.112.3.105

## Slide 115: VPN > IPsec > Tunnels TANet 端

## Slide 116: VPN > IPsec > Tunnels TANet 端

## Slide 117: VPN > IPsec > Tunnels NTU 端

## Slide 118: VPN > IPsec > Tunnels NTU 端

## Slide 119: Firewall > NAT > Outbound NTU 端

## Slide 120: Firewall > NAT > Outbound NTU 端

## Slide 121: 簡報完畢 謝謝